ARPIE / Thankyou for supporting ARPIE! / The information on this page is the bare minimum needed to build the project, however you will find expanded information for building your ARPIE at the following URL https://github.com/hotchk155/arpie/wiki / ARPIE Component Designators / R1, R2, R3, R4, R18 - 220 Ohm (red-red-brown code) resistor / R5, R6, R7, R8 -1.5 kOhm (brown-green-red code) resistor / R9, R10, R13 - 10 kOhm (brown-black-orange code ) resistor / R11, R12, R14, R15, R16, R17, R19, R20 - 1 kOhm (brown-black-red code) resistor / D1, D2 - 1N4148 Small Signal Diode (small orange/black glass package). Align cathode stripe with corresponding marking on PCB. / D3 - 1N4001 Rectifier Diode (black plastic package, silver lettering). Align cathode stripe with corresponding marking on PCB. / C1, C2, C3, C4, (C9) - 100nF Ceramic Capacitor (105 code). C9 is optional and allows auto-reset during firmware upload. / C5, C6 - 33pF Ceramic Capacitor (33 code) / C7, C8 - 4.7uF Electrolytic Capacitor (polarised, check negative terminal marked on package and PCB) / X1 - 16MHz Crystal / TR1 - 2N3904 General Purpose NPN Transistor (polarity matters, check outline on PCB) / Solder the IC sockets before fitting IC's. Check orientation of pin 1 notch/dimple with markings on PCB) / IC1 -ATMega328P Microcontroller with firmware / IC2 - PIC12F1822 Microcontroller with firmware / IC3, IC4 - 6N138/6N139 High Speed Opto-Coupler / Check voltage regulator (IC5) orientation against markings on the PCB / IC5 - 7805-TO220 +5V Voltage Regulator / LEDs – ARPIE uses a row of 16 blue LEDs on the control surface PCB. The control surface has 4 other indicator LEDs (suggested red) and the main board has 3 diagnostic LEDs (suggested green). Feel free to use the supplied green and red LEDs as you wish. Remember the anode (positive) terminal of an LED has the longer lead. / Switches, Battery holder + M2.5 nuts/bolts, Sockets, Pin Headers, Standoff Pillars + M3 bolts – it should be reasonably obvious where all those bits go but if in any doubt please refer to the build instructions at the URL given above. The supplied 6 pin right-angle header is optional and would be soldered in location ICSP1 where it allows upload of new ARPIE firmware via a suitable cable (e.g. FTDI USB2TTL 5V) and Arduino environment. / I hope you enjoy your ARPIE. If you have any problems please contact me at the following email goarpie@gmail.com or via the site where you ordered your ARPIE / ARPIE is an open source, open hardware project. All input is welcome, from wish-list ideas to actual code. Also if you do something amazing with your ARPIE I'd love to see it / Cheers / Jason Hotchk155	ARPIE / Thankyou for supporting ARPIE! / The information on this page is the bare minimum needed to build the project, however you will find expanded information for building your ARPIE at the following URL https://github.com/hotchk155/arpie/wiki / ARPIE Component Designators / R1, R2, R3, R4, R18 - 220 Ohm (red-red-brown code) resistor / R5, R6, R7, R8 -1.5 kOhm (brown-green-red code) resistor / R9, R10, R13 - 10 kOhm (brown-black-orange code ) resistor / R11, R12, R14, R15, R16, R17, R19, R20 - 1 kOhm (brown-black-red code) resistor / D1, D2 - 1N4148 Small Signal Diode (small orange/black glass package). Align cathode stripe with corresponding marking on PCB. / D3 - 1N4001 Rectifier Diode (black plastic package, silver lettering). Align cathode stripe with corresponding marking on PCB. / C1, C2, C3, C4, (C9) - 100nF Ceramic Capacitor (105 code). C9 is optional and allows auto-reset during firmware upload. / C5, C6 - 33pF Ceramic Capacitor (33 code) / C7, C8 - 4.7uF Electrolytic Capacitor (polarised, check negative terminal marked on package and PCB) / X1 - 16MHz Crystal / TR1 - 2N3904 General Purpose NPN Transistor (polarity matters, check outline on PCB) / Solder the IC sockets before fitting IC's. Check orientation of pin 1 notch/dimple with markings on PCB) / IC1 -ATMega328P Microcontroller with firmware / IC2 - PIC12F1822 Microcontroller with firmware / IC3, IC4 - 6N138/6N139 High Speed Opto-Coupler / Check voltage regulator (IC5) orientation against markings on the PCB / IC5 - 7805-TO220 +5V Voltage Regulator / LEDs – ARPIE uses a row of 16 blue LEDs on the control surface PCB. The control surface has 4 other indicator LEDs (suggested red) and the main board has 3 diagnostic LEDs (suggested green). Feel free to use the supplied green and red LEDs as you wish. Remember the anode (positive) terminal of an LED has the longer lead. / Switches, Battery holder + M2.5 nuts/bolts, Sockets, Pin Headers, Standoff Pillars + M3 bolts – it should be reasonably obvious where all those bits go but if in any doubt please refer to the build instructions at the URL given above. The supplied 6 pin right-angle header is optional and would be soldered in location ICSP1 where it allows upload of new ARPIE firmware via a suitable cable (e.g. FTDI USB2TTL 5V) and Arduino environment. / I hope you enjoy your ARPIE. If you have any problems please contact me at the following email goarpie@gmail.com or via the site where you ordered your ARPIE / ARPIE is an open source, open hardware project. All input is welcome, from wish-list ideas to actual code. Also if you do something amazing with your ARPIE I'd love to see it / Cheers / Jason Hotchk155