MODE SHFT SPAN RATE VELO GATE INST SYNC CHAN TRAN ARPIE Quick Reference / Firmware v1.02 / PRESS Arp mode / / Pattern fill Octave shift / output Arp span in / octaves Arp step / length MIDI / velocity MIDI note / length Arp note insert / Chord insert MIDI clock source / internal BPM MIDI output / channel Chromatic transpose output / HOLD Velocity as played / / As selected MIDI Panic Global Options Input Channel/ / OMNI mode / 1 ▬ UP -3 OCT 1 OCTAVE 1 0 1/15 STEP NONE SOURCE Resend Chan.Msg 1 -3 SEMI ▬ 1 / 2 DOWN -2 OCT 2 OCTAVE 2D 15 2/15 HIGHEST SEND Pass Orig Note 2 -2 2 / 3 UP-DOWN -1 OCT 3 OCTAVE 2 23 3/15 LOWEST Pass Orig Chan.Msg 3 -1 3 / 4 RANDOM NORMAL 4 OCTAVE 4D 31 4/15 3FW-1BK 60 BPM Synch from IN 4 NORMAL 4 / 5 ▬ KEYBOARD +1 OCT 2T 39 5/15 4FW-2BK 80 Synch from SYNCH 5 +1 ▬ 5 / 6 +2 OCT 4 47 6/15 100 6 +2 6 / 7 +3 OCT 8D 55 7/15 120 7 +3 7 / 8 4T 63 8/15 140 8 +4 8 / 9 ▬ 8 71 9/15 160 9 +5 ▬ 9 / 10 16D 79 10/15 180 10 +6 10 / 11 8T 87 11/15 RANDOM 200 11 +7 11 / 12 16 95 12/15 Cmin7 220 12 +8 12 / 13 ▬ 16T 103 13/15 Cmaj7 13 +9 ▬ 13 / 14 RANDOM 32 111 14/15 C7 TAP 14 +10 14 / 15 CLEAR 119 FULL Cmin BPM- 15 +11 15 / 16 FILL 127 TIE Cmaj BPM+ 16 +12 16 / ● Press HOLD to toggle chord hold mode. Press and hold to lock MIDI note input (LED flickers). Press HOLD again to unlock. ● Settings stored in EEPROM: Output Channel / Input Channel / Synch Source / Synch Send / Global Options / ● Global Options: Resend non-note channel messages from selected input to selected output channel / Pass through note messages / non-note channel messages received on selected input channel / Accept external synch from MIDI IN / SYNCH port / ● Restore default settings to EEPROM: Hold down HOLD at startup, press MODE then release both buttons. ● Display Firmware Version Hold down HOLD at startup. 4 decimal digits coded in binary (4 bits each). Implied dd.dd format
MODE SHFT SPAN RATE VELO GATE INST SYNC CHAN TRAN ARPIE Quick Reference / Firmware v1.02 / PRESS Arp mode / / Pattern fill Octave shift / output Arp span in / octaves Arp step / length MIDI / velocity MIDI note / length Arp note insert / Chord insert MIDI clock source / internal BPM MIDI output / channel Chromatic transpose output / HOLD Velocity as played / / As selected MIDI Panic Global Options Input Channel/ / OMNI mode / 1 ▬ UP -3 OCT 1 OCTAVE 1 0 1/15 STEP NONE SOURCE Resend Chan.Msg 1 -3 SEMI ▬ 1 / 2 DOWN -2 OCT 2 OCTAVE 2D 15 2/15 HIGHEST SEND Pass Orig Note 2 -2 2 / 3 UP-DOWN -1 OCT 3 OCTAVE 2 23 3/15 LOWEST Pass Orig Chan.Msg 3 -1 3 / 4 RANDOM NORMAL 4 OCTAVE 4D 31 4/15 3FW-1BK 60 BPM Synch from IN 4 NORMAL 4 / 5 ▬ KEYBOARD +1 OCT 2T 39 5/15 4FW-2BK 80 Synch from SYNCH 5 +1 ▬ 5 / 6 +2 OCT 4 47 6/15 100 6 +2 6 / 7 +3 OCT 8D 55 7/15 120 7 +3 7 / 8 4T 63 8/15 140 8 +4 8 / 9 ▬ 8 71 9/15 160 9 +5 ▬ 9 / 10 16D 79 10/15 180 10 +6 10 / 11 8T 87 11/15 RANDOM 200 11 +7 11 / 12 16 95 12/15 Cmin7 220 12 +8 12 / 13 ▬ 16T 103 13/15 Cmaj7 13 +9 ▬ 13 / 14 RANDOM 32 111 14/15 C7 TAP 14 +10 14 / 15 CLEAR 119 FULL Cmin BPM- 15 +11 15 / 16 FILL 127 TIE Cmaj BPM+ 16 +12 16 / ● Press HOLD to toggle chord hold mode. Press and hold to lock MIDI note input (LED flickers). Press HOLD again to unlock. ● Settings stored in EEPROM: Output Channel / Input Channel / Synch Source / Synch Send / Global Options / ● Global Options: Resend non-note channel messages from selected input to selected output channel / Pass through note messages / non-note channel messages received on selected input channel / Accept external synch from MIDI IN / SYNCH port / ● Restore default settings to EEPROM: Hold down HOLD at startup, press MODE then release both buttons. ● Display Firmware Version Hold down HOLD at startup. 4 decimal digits coded in binary (4 bits each). Implied dd.dd format