ARPIE Functions Quick Reference Chart
		MODE	SHFT	SPAN	RATE	VELO	GATE	INST	SYNC		CHAN	TRAN
FUNC		Arp mode / / Pattern fill	Octave shift / output	Arp span in / octaves	Arp step / length	MIDI / velocity	MIDI note / length	Arp note insert / Chord insert	MIDI clock source / internal BPM		MIDI output / channel	Chromatic transpose output
ALT / (hold button)						As Played / Select		MIDI / Panic		Global / Options	input channel/ / OMNI
1	▬	UP	-3 OCT	1 OCTAVE	1	0	1/15 STEP	NONE	SOURCE	IN Note Echo	1	-3 SEMI	▬	1
2		DOWN	-2 OCT	2 OCTAVE	2D	15	2/15	HIGHEST	SEND	IN Other Echo	2	-2		2
3		UP-DOWN	-1 OCT	3 OCTAVE	2	23	3/15	LOWEST		IN Synch	3	-1		3
4		RANDOM	NORMAL	4 OCTAVE	4D	31	4/15	3FW-1BK	60 BPM	AUX Sync	4	NORMAL		4
5	▬	KEYBOARD	+1 OCT		2T	39	5/15	4FW-2BK	80		5	+1	▬	5
6			+2 OCT		4	47	6/15		100		6	+2		6
7			+3 OCT		8D	55	7/15		120		7	+3		7
8					4T	63	8/15		140		8	+4		8
9	▬				8	71	9/15		160		9	+5	▬	9
10					16D	79	10/15		180		10	+6		10
11					8T	87	11/15	RANDOM	200		11	+7		11
12					16	95	12/15	Cmin7	220		12	+8		12
13	▬				16T	103	13/15	Cmaj7			13	+9	▬	13
14		RANDOM			32	111	14/15	C7	TAP		14	+10		14
15		CLEAR				119	FULL	Cmin	BPM-		15	+11		15
16		FILL				127	TIE	Cmaj	BPM+		16	+12		16

● Settings stored in EEPROM: Output Channel / Input Channel / Synch Source / Synch Send / Global Options ● Restore default settings to EEPROM: Hold down HOLD at startup, press MODE then release both buttons.
● Display Firmware Version Hold down HOLD at startup. 4 decimal digits coded in binary (4 bits each). Implied dd.dd format