# ARPIE RELEASE NOTES REL 8 BETA XXXXX2014
# NEW FEATURE: SYNCH PULSE
A news options in "global preferences" menu has been added. This is accessed with a long press to the PLEN menu button. These options are save to EEPROM

Hack Header					Auto revert	Long Press		LED Profile
Bit 7	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0					A	B	A	B

0	0	a	a	x	x	x	x	PC5 Analog Input Mode / 0 0 Disable / 0 1 Transpose Pot / 1 0 Tempo Pot / 1 1 CC#16 Pot
0	0	x	x	b	b	x	x	PC4 Analog Input Mode / 0 0 Disable / 0 1 Velocity Pot / 1 0 Pitch Bend Pot / 1 1 CC#17 Pot
0	0	x	x	x	x	c	c	PC0 Analog Input Mode / 0 0 Disable / 0 1 Mod Wheel Pot / 1 0 Gate Length Pot / 1 1 CC#18 Pot
0	0	0	0	0	0	1	1
0	0	0	0	0	1	0	0
0	0	0	0	0	1	0	1

# ARPIE RELEASE NOTES REL 7 BETA XXXXX2014
# IMPROVEMENT: REVERT TO PRIMARY MENU FUNCTION
Holding a menu button for the "long press period" provides (for some menu buttons) a secondary menu function, which remains active until another menu button is pressed. In previous versions it was not possible to press the same menu button again to revert from "long press mode" to the "standard mode" for that menu button.
This is improved in this release - once latched with a "long press" into a secondary menu function, you can press the same menu button again to go back to the primary menu function.
Only the primary menu function auto reverts back to PATN mode. The secondary menu function remains active until another function is selected.
# NEW FEATURE: GLIDE
Notes which start playing at a step for which GLIDE is enabled (In the display accessed by holding PATN where PATN secondary function is GLIDE EDIT) will
- Override the GATE setting and play for one full step (GLIDE TIE mode OFF)
- Override the GATE setting and play until the next note starts playing (GLIDE TIE mode OFF)
# NEW FEATURE: ACCENT
Notes which start playing at a step for which ACCENT is enabled (In the display accessed by holding PATN where PATN secondary function is ACCENT EDIT) will play at full MIDI velocity (127) regardless of the current VELO setting or note input velocity.
# NEW FEATURE: STACK
When a note starts to play at a step for which STACK is enabled, the note at the next step will start to play at the same time. If STACK is also enabled for the following step then that note will also play (and so on). The result is a chord built from these notes.
- The GLIDE and ACCENT settings for the first note in the stack are applied to all the stacked notes (i.e. GLIDE and ACCENT are ignored for any step where the previous step had NOTE STACK applied)
- Gated Chord arpeggio mode takes precedence over STACK. In this mode the STACK settings are ignored
# NEW FEATURE: SELECT PATN KEY SECOND FUNCTION
The "Performance options" menu (accessed with a long press to the MODE menu button) have been extended as shown below. These options are saved to EEPROM
Hold Button Fn 2		Skip On Rest	Tie Notes On GLIDE	Secondary PATN function

- Tie Notes On GLIDE controls an aspect of GLIDE mode (see above)
- When Edit GLIDE is lit, the secondary function of the PATN menu button is to edit GLIDE mode
- When Edit GLIDE is unlit, the secondary function of the PATN menu button is to edit ACCENT mode
- By default the secondary function of the PATN menu button is to edit GLIDEmode
GLIDE and ACCENT sequences remain active for playback even when they are not available to edit
# ARPIE RELEASE NOTES REL 6 BETA 19MAY2014
# IMPROVEMENT: MIDI STOP AND CONTINUE
Arpie now detects MIDI STOP and CONTINUE events coming from the external MIDI synch port and will stop playback after a STOP even if the MIDI beat clock continues.

# NEW FEATURE: FORCE TO SCALE
Force to scale is accessible by pressing and holding the SPAN button

SCALE TYPE					OFF-SCALE NOTE ADJUST
Chromatic	Ionian	Dorian	Phrygian	Lydian	Mixolydian	Aeolian	Locrian				Ignore (No Rest)	Mute (Rest)	Flatten	Sharpen	Alternate

Notes output by the arpeggiator are adjusted (if neccessary) to fall on the scale defined by the key root note (see below) and the scale type. Out of scale notes can be skipped (with or without a rest) or sharpened/flattened by 1 semitone to bring them on to the scale. The Alternate mode sharpens and flattens alternate off-scale notes in the arpeggio sequence. Each time the arpeggio is rebuilt the adjustment applied to each note is also toggled. You can force a rebuild by pressing Alternate while the arpeggio is playing. The adjustment is also alternated with each octave in the arpeggio sequence (so in a sequence spanning 2 octaves notes which are sharpened on the first octave are flattened in the second and vice-versa)

Chromatic	C	C#	D	D#	E	F	F#	G	G#	A	A#	B
Ionian	C		D		E	F		G		A		B
Dorian	C		D	D#		F		G		A	A#
Phrygian	C	C#		D#		F		G	G#		A#
Lydian	C		D		E		F#	G		A		B
Mixolydian	C		D		E	F		G		A	A#
Aeolian	C		D	D#		F		G	G#		A#
Locrian	C	C#		D#		F	F#		G#		A#

The scale root note is selected by pressing and holding the SHFT button

SCALE ROOT NOTE
C	C#	D	D#	E	F	F#	G	G#	A	A#	B

# NEW FEATURE: PREFERENCES
A new "global preferences" menu has been added. This is accessed with a long press to the PLEN menu button. These options are save to EEPROM

Auto revert	Long Press		LED Profile
	A	B	A	B

Auto Display Revert determines whether the display reverts to "pattern" display
OFF = do not revert
ON = revert back after approx 10 seconds

Long Press Time selects the amount of time that a menu button needs to be held down in order to access "second function"
A = OFF, B=OFF - 1.5 seconds
A = ON, B=OFF - 1 second
A = OFF, B=ON- 0.5 seconds
A = ON, B=ON- 0.25 seconds

LED Profile allows a choice between different sets of LED brighness levels. Select the best option for the LEDs you have installed on your ARPIE, where you have a decent contrast between the DIM, MEDIUM and BRIGHT options without excessive flickering. As a guideline:
A = OFF, B=OFF - Use with super high brightness LEDs (e.g. super bright white/green)
A = ON, B=OFF - Use with high brightness LEDs (e.g. super bright blue)
A = OFF, B=ON - Use with medium brightness LEDs (e.g. bright blue/red)
A = ON, B=ON - Use with low brightness LEDs (e.g. standard green)

# NEW FEATURE: PERFORMANCE OPTIONS
A new "performance options" menu has been added. This is accessed with a long press to the MODE menu button. These options are saved to EEPROM
Hold Button Fn 2		Skip On Rest

Hold Button Secondary Function controls what happens when the hold button is held for a long period of time and starts flashing.
OFF = MIDI Lockout (normal function)
ON = MIDI Transpose (New feature - see below)

Skip On Rest controls how the arpeggio sequencer handles "rests" in the rhythmic pattern
OFF = Notes from the arpeggiated sequence are not skipped when they coincide with a rest in the patten editor. The current position in the sequence increments only when notes are played (New feature - see below)
ON = Notes from the arpeggiated sequence are skipped when they coincide with a rest in the patten editor. The current position in the sequence increments at every step whether the note is played or note (normal function)
# NEW FEATURE: TRANSPOSE BY MIDI INPUT
This new option allows you to tranpose a held arpeggio using your MIDI keyboard. You select the mode by
- Selecting "MIDI Transpose" as the secondary HOLD button function in the preferences menu (This setting is saved when power is off)
- Holding an arpeggio using a single press of the HOLD button then pressing the HOLD button again and keeping it pressed until the HOLD LED starts to flash
Now pressing a key on your MIDI keyboard will transpose the held arpeggio. ARPIE takes the lowest note in the held chord as its root note, and transposes the chord to root it on the note you pressed.
To exit MIDI transpose, press the HOLD button once. Press it again to clear the held chord.
MIDI tranpose can be used interchangeably with the TRAN menu,
Pressing the same tranpose key repeatedly will rebuild the arpeggio, retriggering any "random" chord ordering or "alternating" force to scale setting.
# NEW FEATURE: SKIP ON REST OPTION
Usually when ARPIE encounters a reset in the current pattern position, the current note from the arpeggiator sequence is skipped (muted)
This behaviour can now be controlled by a new option. When the option is set (by default) the usual behaviour is observed however, if the option is unset, the note which coincides with the mute is not skipped but is played on the next pattern note, so no notes from the arpeggio are skipped.
# NEW FEATURE: POLYPHONIC CHORD GATE
A new option has been added to the ARP mode menu
ARP MODE					PATTERN
UP	DOWN	UP-DOWN	RANDOM	KEYBOARD	POLY GATE					RANDOM	CLEAR	FILL

In this mode, all notes of the arp sequence play together as a single chord, which is gated according to the pattern of beats and mutes.